## Slide 1
A Regulators Workshop:
Water Conservation,
Efficiency and
Reuse in California Codes
Michael L. Nearman
Deputy Executive Director
California Building Standards Commission
Sustainable Silicon Valley presents:

## Slide 2
Session Goals
    Environmental policies behind CALGreen
    California code development processes
    Nonresidential Code updates
      2016 CALGreen Code
      Emergency Regulations
    What’s coming in future code cycles?
    Q & A

## Slide 3: Environmental policies behind CALGreen
    CBSC was directed to develop green building standards in response to California’s landmark initiative AB 32 (California Global Warming Solutions Act of 2006)
      A comprehensive program to reduce greenhouse gas emissions (GHG) to 1990 levels by 2020

## Slide 4: Environmental policies behind CALGreen
Goal: Lessen impact buildings have on the environment
  2008: First CALGreen voluntary publication
    (effective August 2009)
  2010, 2013 & 2016: CALGreen Code publications
    Increased requirements

## Slide 6: California Code Development Processes
Intervening Code Cycle timeline (18 months)
  Pre-cycle code development/workshops
  State agency code proposals
  Code Advisory Committee Reviews (6)
  Public comment periods (45 and15 day)
  Final submittals following Public comment period
  CBSC review and approval June 2017
    Codification: file with Secretary of State
  Publication Jan. 2018
    180 days prior to effective date July 2018

## Slide 7
California Building Standards Code
Title 24, California Code of Regulations
  CALGreen is Part 11 of Title 24
    Includes mandatory and voluntary measures
  Occupancies affected by CALGreen:
      Residential
      Nonresidential
      Schools
      Hospitals/Clinics

## Slide 8
California Building Standards Code
Title 24, California Code of Regulations
  Part 1 Administrative Code
  Part 2 Building Code
  Part 2.5 Residential Code
  Part 3 Electrical Code
  Part 4 Mechanical Code
  Part 5 Plumbing Code
  Part 6 Energy Code
  Part 7 Vacant
  Part 8 Historical Building Code
  Part 9 Fire Code
  Part 10 Existing Building Code
  Part 11 Green Building Standards Code (CALGreen)
  Part 12 Referenced Standards Code

## Slide 9
CALGreen Code Format
Chapter 1 Administration
Chapter 2 Definitions
Chapter 3 Green Building
Chapter 4 Residential Mandatory Measures
Chapter 5 Nonresidential Mandatory Measures
Chapter 6 Referenced Organizations and Standards
Chapter 7 Installer and Special Inspector Qualifications
Chapter 8 Compliance Forms and Worksheets
Appendix A4 Voluntary Tiers (Residential)
Appendix A5 Voluntary Tiers (Nonresidential)

## Slide 10
Chapter 1 - Administration
  Purpose
    Minimize impact of building construction on the environment
      Improve construction practices
      Reduce greenhouse gases and air pollution
      Improve indoor air quality
      Reduce use of potable water and incorporate alternative water sources
  Scope
    Application
    Not intended to be identified as meeting the requirements of a point rated system

## Slide 11
Chapter 1 - Administration
  Local amendments based on findings
    Climate
    Topography
    Geology
  Alternative materials and methods
  Construction documents
  Application and state agency authorities

## Slide 12
Chapter 3 – Green Building
  Scope
    301.3 Nonresidential additions and alterations. [BSC-CG]
    Newly constructed buildings [N] or additions and alterations [A].
      When the code section applies to both, no banner will be used.
    Restrictions on plumbing fixtures in accordance with Civil Code Section 1101.3 (AB 723)

## Slide 13
NONRESIDENTIAL

## Slide 14
Chapter 5- Nonresidential
Mandatory Measures
  Planning and Design – Division 5.1
  Energy Efficiency – Division 5.2
  Water Efficiency and Conservation – Division 5.3
  Material Conservation and Resource Efficiency – Division 5.4
  Environmental Quality – Division 5.5

## Slide 15
Chapter 5- Nonresidential
Left column:
2013 current code with intervening amendments
Effective dates-
Triennial: 1/1/2014 Intervening: 7/1/2015
Right column:
2016 Triennial Code
Effective date-
Triennial: 1/1/2017
Preface:
Please note the following effective dates throughout this presentation:

## Slide 16
Chapter 5- Division 5.3
Emergency regulations impacting
2013 CALGreen
Via 2013 Emergency:
Wall mounted urinals reduced to 0.125 gpf, and floor mounted urinals remain at 0.5 gpf
Outdoor potable water use regulations are now aligning with MWELO as updated in July 2015
CEC prohibition of sale or installation of non-compliant fixtures as of Jan. 2016

## Slide 17
Chapter 5 - Division 5.3 Indoor Water Use
2013 Current
“Faucets and Fountains” added prescriptive only flow rates for fixtures in Section 5.303.3.4
Plumbing fixtures and fitting (standards) - CPC
2016 Code
Minor change to metering faucets for wash fountains; clarified gpc (gallons per cycle) instead of gpf (gallons per flush)
New code section: 5.303.4.1 Food Waste Disposers
  Less than 1gpm when not in use
  Auto shut-off after 10 min.
  No more than 8 gpm in normal use
Minor editorial 2016 CPC reference updates

## Slide 18
NONRESIDENTIAL VOLUNTARY MEASURES
Appendix A5
  The measures contained in the appendix are not mandatory unless adopted by a city, county, or city and county. Appendix provisions may also be used voluntarily by designers, builders, and property owners.
  CALGreen Tier 1 and Tier 2 are intended for adoption by cities, counties, and cities and counties to help California meet its goals for greenhouse gas emission reduction.

## Slide 19
Chapter A5 - Voluntary Code
2013 Current
  A5.303.3 Appliances and fixtures for commercial application
  2016 Code
  Increases water use efficiency
    Food Steamers – no more than 2 gph
    Combo Ovens – no more than
    1.5 gph
  New Section: A5.303.3
    Food Waste Pulping Systems – no more than 2 gpm of potable water

## Slide 20
Chapter A5- Voluntary Code
2013 Current
  Commercial dishwasher water use Table A5.303.3
  2016 Code
  Updated table to meet Energy Star requirements for water use
  New section: Nonwater supplied urinals (Definition for Hybrid added to Ch. 2)

## Slide 21
2016 Intervening Code Cycle
Proposed Amendments
2016 Current
  SWPPP (Storm Water Pollution Prevention Plan)
  Shower head flow rate 2 gallons @ 80psi
  2016 Code
  Added new pointers to existing laws for SWPPP
  New flow rate: 1.8 gallons @ 80psi to align with CEC
  Title 20 standards

## Slide 22
California Building Standards Commission
Use the web! www.bsc.ca.gov
    Rulemaking processes
    Code cycles
    Current codes
    Guidebooks and other resources
    Information Bulletins
    Commission meeting notices and agendas
    Newsletters

## Slide 23
California Building Standards Commission
Guide to the 2016 California Green Building Standards Code - Nonresidential
    Available January 2017
    Includes new Verification Guidelines

## Slide 25
Additional questions about the California Codes?
Contact CBSC!
California Building Standards Commission
2525 Natomas Park Drive, Suite 130
Sacramento, CA 95833
(916) 263-0916
cbsc@dgs.ca.gov